A . Features

- 6 Digits LCD Display，Display Hour ,Minute ,Second ,Month ,Day and Week

- Daily Alarm and Chime hourly

- Snooze

- 12 / 24H format selectable，Auto Calendar

- 1/100 second Chronograph with split functions

- EL backlight

B . Operational Manual

- At any state ,press Ａ key EL backlight for 3s .

- Real Time

- Press Ｃ key to display Alarm ;Press Ｄ key to display Date .

- Turn On / Off Alarm and Chime

a). Press Ｃ＋Ｄ key to turn on / off Alarm ,indicator “      ”displaying for On .

b). Press Ｃ＋Ｂ key to turn On / Off Chime ,all days of week displaying for On .

- Chronograph

- The display range of the Chronograph is 23 hours ,59 minutes ,59.99 seconds.

- Press Ｄ key to Start/Stop running ;

- When stop ,press C  key to zero .

- When running ,press Ｃ key to split count.

- Then press Ｄ key to exit split count ,and stop counting ;

- When exit split count ,press Ｃ key to display all counts ; and press Ｃ key again to zero ;

- When running ,press Ｂ key to return to Real Time Mode ,and it running at back .

- Daily Alarm

- "Hour " flashing once entry Daily Alarm .

- Press C key to select "Hour " or "Minute "setting

- Press D key to adjust the flashing item

- Press C key to confirm

- Press Ｂ key to return to Real Time mode

- Alarm Snooze ON/OFF

At Alarm sounding state ,press Ｃ key to stop sounding ,and press Ｄ key to ON/OFF snooze function .When Snooze function be ON ,it will sound five minutes later ,and auto stop after sounding for a minute .

- Time Setting

"Second " flashing when loading ,press D key to zero ; Press C key to select item as following sequence :

Minute     Hour     Day      Month     Week

- Press Ｄ key to adjust the flashing item.

- When setting "Hour " ,"Ｈ" display for ２４H format ;"Ａ" or "Ｐ" for １２H format .

- Press D key while the seconds are in the range of 30 to 59 resets them to 00 and adds 1 to the minutes . In the range of 00 to 29,the minutes are unchanged.

C. Specifications

- Module Size

- Module Thickness

- Operational Temperature Range

- Operational Voltage

- Accuracy

- Battery Code

- Current Consumption for Digit（maxima）

- Current Consumption for Digit（averagely）

- Alarm Current

- EL Current

- Battery life

# Text boxes

：mm

：8.15±0.15 mm

：-10℃~60℃

：3.0V

：±90sec/month

：CR2016

：≤3.5 u A(T=25℃)

：≤2.5 u A(T=25℃)

：≤2.5 m A

：≤10 m A

：18 month(Japan Lithium)

|  | Prepared | Checked | Approve |
| --- | --- | --- | --- |
| Name | 冯碧颜 | 徐治中 | 宋检望 |
| Date | 08/03/20 | 08/03/20 | 08/03/20 |

LMODE（B Key）

LIGHT（A K	ey）

（C Key） RESET

（D Key） START

Real Time

Time setting

Alarm

Chronograph

B Key

B Key

3 backlight operation (6 seconds) per day

20 seconds of alarm operation per day

B Key